## Slide 1
数値シミュレーションレーションによる
粉末金型充填における吸引効果の影響
○吉田昂生1 森勇稀1 高畑和弥1 酒井幹夫2*
1. 東京大学大学院工学系研究科原子力国際専攻
化学工学会関東支部横浜大会
分類 : 6-f 情報処理技術
2019/8/8
2. 東京大学大学院工学系研究科レジリエンス工学研究センター

## Slide 2: 研究背景
・粉末金型充填
錠剤の生産プロセスの一部。充填の後に圧縮・排出を経て錠剤は生産されている。
粉末は充填中に空気抵抗を受けるため、充填には時間がかかりプロセス全体のネックになっている。
Tablet
(www.pakutaso.com)
Rotary Tablet Press Machine
(Copyright © 2003 HATA TEKKOSHO CO.,LTD. All rights reserved.)
・吸引効果
粉末の下に設置した杵を降下させることにより粉末が金型内に引き込まれる効果。
充填完了時間を短縮する効果があるとされている。
吸引効果の図
Punchの降下アニメーション？
Notes: 配置をZ型に

## Slide 3: 先行研究・本研究の目的
実験において、下杵の降下による吸引効果が充填完了時間を短縮できることが確認された。降下速度の影響は不明。 [1]
下杵の降下速度と充填完了時間の関係が明らかにすることが生産プロセスの効率化につながる。
実験では吸引効果の影響を詳細に把握することが難しい。
✔ 吸引効果で充填完了時間が短く
✗ 下杵の降下速度と充填完了時間の関係性
[1] S. Jackson, I.C. Sinka, A.C.F. Cocks, 2006
下杵の降下速度が充填完了時間に及ぼす影響を明らかする
✎ 本研究の目的
下杵降下速度が伝わるもの
Notes: It could be assumed that air pressure gradient accelerated the influx of the powder and shortened the filling time [1] .
But how pressure gradient affected the powder movement has not been clarified so far.

## Slide 4: 解析手法
✗ 移動する壁面の扱いが難しい
数値シミュレーションにおいて、移動する壁面の境界条件は複雑になりやすく、扱いが難しい。
Immersed Boundary Method (IBM)[1]
[1] C.S. Peskin, 1972
Gas Phase
Wall Region
IBM Field
の壁面の割合
速度
グリッド内の壁面の割合を用いて、気相の境界条件を定義。
シンプルなアルゴリズムで計算が可能。
気相の支配方程式
速度
壁面の移動がつたわるもの
Notes: 5分
Signed Distance Function
Boundary is defined by the scalar field of the distance from wall. With this scalar field, it is easy to calculate the interaction between a particle and a wall.
ImmersedBoundary Method
The interaction between the gas phase and a wall is calculated only by ratio of the wall in a staggered grid. The ratio is obtained easily by Signed Distance Function.
This combination of boundary conditions enables it easy to calculate interaction with wall in arbitrary wall shape, only with very simple algorithms.

## Slide 5: 解析条件
下杵の降下速度100, 200, …., 700 mm/s の7ケースで比較を行った。
Gas phase | 
Viscosity | [Pa・s]
Density | 1 [kg/m3]
Solid phase | 
Density | 1500 [kg/m3]
Spring constant | 50 [N/m]
Coefficient of restitution | 0.9
Coefficient of friction | 0.3
Gas phase | 
Viscosity | 
Density | 1 [kg/m3]
Solid phase | 
Density | 1500 [kg/m3]
Spring constant | 50 [N/m]
Coefficient of restitution | 0.9
Coefficient of friction | 0.3
Diameter of particles | 250 [μm]
Number of particles | 500,000
System | Mono-dispersed
Grid size | 0.5 [mm]
Calculation time | 0.24 [s]
Physical Properties
Calculation Conditions
Punch
Schematic Geometry
Unit : mm
Initial Position of Particles

## Slide 6: 結果・考察
下杵の降下速度に対して充填完了時間は極小値をとる
粒子流入の深さが違う
充填量に差がない
originality

## Slide 7: 結果・考察
100 mm/s
300 mm/s
500 mm/s
700 mm/s
Fluxが最初に高いこと。速度に比例して高いこと。
後半に500のフラックスが上がること
Die領域を示した図。
or 動画中のDie領域を指し示す。

## Slide 8: 結果・考察
粒子が下杵に追いつく
粒子と下杵の間に隙間
下杵の降下速度が大きいと空気が多く入る

## Slide 9: 結果・考察
気泡が分裂して抜けていかない
気泡が塊で抜けていく
下杵の降下速度が大きいと気泡の抜けが遅れる

## Slide 10: 結論
下杵の降下速度が充填完了時間に及ぼす影響を明らかする
✎ 本研究の目的
[1] S. Jackson, I.C. Sinka, A.C.F. Cocks, 2006
あああああ
✔ 充填完了時間はある速度で極小値をとる
あああああ
✔ ああああああああああああ
あああああ
✔ あああああああああ
originality
Notes: It could be assumed that air pressure gradient accelerated the influx of the powder and shortened the filling time [1] .
But how pressure gradient affected the powder movement has not been clarified so far.

## Slide 11
0.174 s
Approx. 83%
0.210 s
In case suction, powder filling took 83% time compared with case gravity. The suction effect shortened the powder filling time.
The times particles had filled 99% in each case are written.
In case suction, the flux of powder flow increased rapidly compared with case gravity. The suction effect accelerated the flux of powder.
Results & Discussion (Quantitative Evaluation)
The flux increased rapidly and the filling time was shortened
Flux of Particles [1/s・mm2]
Notes: 9, 10分ぐらいで、このCaseが終了したらいいかんじ。

## Slide 12: Numerical Method
Solid Phase : DEM[2]
Gas Phase : CFD + Local Average Volume3]
+
Exchange of momentum
[1] Y. Tsuji et al., Powder Tec. (1993).
[2] P.A. Cundall and O.D. Strack, Geotechnique (1979)
[3] T.B. Anderson and R. Jackson, Ind. Eng. Chem. Fundam. (1967)
・Modeling of solid phase and gas phase
In this study, for modeling solid-gas phase interaction DEM-CFD method[1] (Discrete Element Method - Computational Fluid Dynamics) was used. (Particles are modeled by DEM, Air is modeled by CFD)

## Slide 13: Numerical Method
Solid Phase : SDF[1]
Gas Phase : IBM[2]
[1] Y. Shigeto et al, Chem. Eng. J. (2013).
[2] C.S. Peskin, J. Comput. Phys. (1972).
+
Signed Distance is changing with wall moving
・Boundary Conditions
In this study, we used Signed Distance Function[2] and Immersed Boundary Method[3] combinedly to calculate moving boundary in gas-solid flow. This combination of boundary conditions had verified.[4][5]

## Slide 14: 解析手法
・Modeling of solid phase and gas phase
In this study, for modeling solid-gas phase interaction DEM-CFD method[1] (Discrete Element Method - Computational Fluid Dynamics) was used. (Particles are modeled by DEM, Air is modeled by CFD)
[1] Y. Tsuji et al., Powder Tec. (1993).
[2] Y. Shigeto and M. Sakai, Chem. Eng. J. (2013).
・Boundary Conditions
In this study, we used Signed Distance Function[2] and Immersed Boundary Method[3] combinedly to calculate moving boundary in gas-solid flow. Only with simple algorithms, this combination enable to calculate interaction with wall in arbitrary shape. This combination of boundary conditions had verified.[4][5]
Solid Phase : SDF (Signed Distance Function)
Gas Phase : IBM (Immersed Boundary Method)
SDF Field
[3] C.S. Peskin, J. Comput. Phys. (1972).
[4] Y. Mori et al., Powder Tec. (2019).
Gas Phase
Wall Region
IBM Field
[5] H. Yao et al., J. Taiwan Inst. Chem. Eng. J. (2018).
+
Notes: 5分
Signed Distance Function
Boundary is defined by the scalar field of the distance from wall. With this scalar field, it is easy to calculate the interaction between a particle and a wall.
ImmersedBoundary Method
The interaction between the gas phase and a wall is calculated only by ratio of the wall in a staggered grid. The ratio is obtained easily by Signed Distance Function.
This combination of boundary conditions enables it easy to calculate interaction with wall in arbitrary wall shape, only with very simple algorithms.